## Slide 1
FEATURES
· 15” High Performance Coaxial Driver
· Premium Baltic Birch PlyWood Enclosure (18T)
· Dedicated Passive Network
· Provide DSP Data
· Bi-amp&Passive Mode Switch
KM5
KOOON Audio l 160-1, Jong-ro, Jongro-gu, Seoul l Rep. of Korea
Tel 010 5223 5997 l www.kooon-audio.com
PRODUCT
- we connect sound to the community -
SPECIFICATIONS
· Type : Passive
· Sensitivity(1W/1m) :98dB
· Frequency Range(-10dB) : 87Hz~17kHz
· Max SPL(Peak) : 130dB
· AES Power / Program Power / Peak Power : 400W / 800W / 1600W
· Dispersion Angle(Horn) : (HxV) : 86˚x64˚(1kHz) / 72˚x64˚(4kHz)
· Normal Impedance : 8Ω
· Weight : 20.80 kg
· Dimensions(WxHxDmm) : 582x361x512mm
· Connection : 2 X SPEAKON [Parallel] Bi-Amp(1±,2±)/Passive(1+,1-) Switch
· Painting : Polyurea Coating
ImP